Gun does not operate target

Is there a gun noise when the gun is operated ?

# Yes

# Is there a blockage in the gun barrel?

Yes				No

Remove the blockage	Is the purple wire through the gun

Broken?

Yes	            No

Replace broken wire         Change gun circuit

board

Does system work

Yes      		No

Repair circuit board	Remove gun barrel

Has the emitter lens

Become detached?

Yes	           No

Refix lens	Replace emitter,

Observing correct

Polarity.(hole at top

Pink wire on right)

No

Check fuse on circuit board

Check speaker

## Remove trigger assembly

And check the operation of

The switch with an electrical

Meter.

Does the switch work?

Yes		No

### Is the purple or	    replace switch

Pink wire through

The gun hose broken?

Yes	           No

Replace wires                Replace gun board

21/4/06